# Rotary Hoe Pro Adjustment
Thaddeus Hughes
20 AUG 2024
# Is the center pivot strong enough?
Some ideas here depend on the center pivot of the rotary hoe being strong enough to withstand all bending loads without the help of the mounting flange. The shaft and the bearing surface seem amply large – but the connection to the formed crossmember is suspect.
Upgrading the formed crossmember to a box tube, and running the pivot axle through both walls of the box tube, would dramatically strengthen this joint, but does raise some issues with mounting the fingers that go between the hoes.
# Idea 1: Quick-Adjust Handles
Instead of nuts, use quick-adjust handles such as McMaster-Carr 64835K82. On these, the operator can pull the handle upwards to adjust the angle of the handle without tightening or loosening the threads. You could put tabs that the handle would sit in so that it won’t vibrate loose.
My thoughts: This is simple, and certainly makes adjustment easy, but I don’t know that enough torque will be generated to hold if a slot is used. Not sure what the load rating is.
# Idea 2: Quick-Adjust Handles With Countersinking Locks
Same as idea 1, but include some tapered bushings between the handles and the plate. These would taper-lock into a series of countersinks when tightened down.
My thoughts: Adds a milling operation to an otherwise laser-cut part. Custom components. Doesn’t add that much locking with the fine adjustments needed.
# Idea 3: Quick-Adjust Center with Pins
This idea requires the center pivot to support all bending loads.
Replace the threaded studs with dowel pins. The dowels would be permanently pressed into the bottom bracket. The top bracket would contain a series of holes that these dowels could slip into on the top.
Capping the center pivot itself would be on an over-center handle, so that the operator could flip up the handle and “drop” the hoe wheel bracket. Once dropped, the hoe wheel bracket could be rotated until a new set of holes and pins are lined up, and then flip down the handle. This would engage the new set of holes and pins.
My thoughts: This requires the pivot joint to be good not only rotationally, but axially. This adds a few more parts. I don’t know how good this will lock the hoe wheel rotationally so that wobble at 0 degrees won’t be a problem.